## Slide 1: NITRIFICATION
da Silva, ME 16052430
Gonde, L 17046832

## Slide 2: WHAT IS NITRIFICATION?
Defined as the oxidation of ammonia to nitrite followed by the oxidation of nitrite to nitrate
Usually occurs in separate organisms
Can also occur as direct ammonia oxidation to nitrate in comammox bacteria
Comammox bacteria is any bacteria that can convert ammonia to nitrate through nitrification
1

## Slide 3: NITRIFICATION SIMPLIFIED
Step 1
Step 1
Ammonium (NH4+)
Step 2
Step 2
Nitrite (NO2-)
Step 3
Step 3
Nitrate (NO3-)
Oxidation
Oxidation
Notes: List all of the steps used in completing your experiment.
Remember to number your steps.

## Slide 4: WHY IS IT USEFUL?
Ammonia is the most reduced form of nitrogen in soil
Nitrate is the most oxidised form of soil nitrogen
The most preferred chemical form of nitrogen uptake from soil or water for most plants is in the form of nitrate
Nitrification converts the most reduced form of soil nitrogen to its most oxidised form

## Slide 5: NITRIFICATION IN AQUAPONICS
This process drives most aquaponic processes
Ammonia in the system must be converted for the plants
Otherwise, plants can suffer from ammonium toxicity
But there are no fish in hydroponics, so no ammonia is formed

## Slide 6: NITROGEN CYCLE
Nitrogen fixation
Nitrification
Assimilation
Ammonification
Denitrification

## Slide 7: ALTERNATING AEROBIC AND ANAEROBIC (AAA)
Nitrification is aerobic
  NH4+ → NO3-
  Autotrophs
Denitrification is anaerobic
  NO3- → N2
  Heterotrophs

## Slide 8: POSSIBLE CONTROL STRATEGY
Ammonia analyser & Nitrate analyser
  Online measurements
  High maintenance
Model-based control strategy
  Predict the ammonia and nitrate amounts
  Good models are complex models
Interpret a signal from online NADH sensors
  Need personnel who can expertly do this
1
3
2

## Slide 9: POSSIBLE CONTROL STRATEGY
Using the ORP and pH profiles there are several points to take note
On the pH profile
  Ammonia valley: Local min
  Nitrate apex ↔ Nitrate knee
On the ORP profile
  Nitrate knee: Point where NO3- is
  significantly removed
  DO elbow ↔ Ammonia valley
4

## Slide 10: USING THE pH PROFILE
Ammonia valley tells one:
  End of nitrification
  End of aerobic period
  Start anaerobic period
Nitrate apex tells one:
  Corresponds to the nitrate knee
  End of denitrification
  End anaerobic period
  Start aerobic

## Slide 11: REFERENCES